Department of theoretical physics and astrophysics of science faculty of Masaryk university in Brno

Physics laboratory III

2, Study of thermoelectron emission on anode

By: Miroslav Štangler	Measured on: 22nd March 2012
Field of study: Astrophysics Year of study: 2011/2012 Semester: IV

Tasks:
1, Measure work w of wolfram by Richardson-Dushman line.
2, Calculate intensity of electric field near the surface of cathode.
3, Measure dependency of Inas = f(Ua) for Ua < 150 V, process it in coordinates ln(Inas) = √Ua and determine increment of current due the presence of electric field for Ua = 150 V. Compare experimentally obtained value with value determined by equation: %DELTA I_{nas} = I_{nas} (e^{{w_{p}} over {kT} } - 1) = BT^{2}e^{{w_{p}} over {kT} }(e^{{w_{p}} over {kT} } - 1)
4, Measure zone of starting current and make a graph for two values of incandescent current If. Do the same for coordinates ln I = f(Ua) and determine temperature of electrons.

1, Richardson-Dushman equation:
I_{nas} = BT^{2}e^{-{w} over {kT} }
ln({I_{nas}} over {T^{2}}) = - {w} over {k} {1} over {T} + ln(B)
Work is slope of this function for values of Inas, T, k and B are constant. We need to calculate temperature T from this formula:
R_{t} = {%rho cdot d} over {S} (1 + %alpha T)
where ρ = 4,89x10-8 Ωm, α = 4,83x10-3K-1, d = 15x10-3 m and S = πr2 = 7,854x10-9 m2.
Temperature of wolfram cathode for Ua = 15 V and lowest current is 1903 K. The rest of value can be seen in table below:

The slope of Richardson-Dushman line is -82992,39362 which is equal to -w/k where k is Boltzmann constant. Work w is then 1,1458x10-18 J = 7,15 eV.

2 & 3, Intensity of electric field is defined as:
E = U_{a} {1} over {r cdot ln(R/r)}
where R = 0,7 mm and r= 0,005 mm. For maximal Ua = 150 V we get E = 6,071x106 Vm-1. The decrease of work is then:
w_{p} = sqrt{{e^{3}E} over {4 %pi %epsilon_{0}} }
wp = 1,498x10-20 J = 0,093 eV.
%DELTA I_{nas} = I_{nas} (e^{{w_{p}} over {kT} } - 1) = BT^{2}e^{{w_{p}} over {kT} }(e^{{w_{p}} over {kT} } - 1)
Due to measuring components we were able to measure Ua only from -50 V to 50 V.
ΔInas = 0,22 μA

From this graph I acquired work by this formula:
w_{p} = (A sqrt{U_{a}} - B) kT = 0,0214 eV

Conclusion:
In this laboratory we measured work w = 7,15 eV, intensity of electrical field
E = 6,071x106 Vm-1. We determined current addiction ΔInas = 0,22 μA. And at last we found out work decrease wp = 0,0214 eV.

Appendix: